## Slide 1: Free-Fall detector
DGMD-E13 Introduction To Wearable Devices, The Internet Of Things, And Machine Learning
Corbett Weinberg

## Slide 2: Motivation
Prevent cell phone damaged from a fall
It’s estimated that in 2017 Americans spent over $3 million on screen damage
  https://www.marketwatch.com/story/americans-spent-over-3-billion-last-year-fixing-their-smartphone-screens-2018-11-20

## Slide 3: Project & Learning Goals for this project
Detect a free fall is occurring based on acceleration data
Hands on leaning of the machine learning python libraries
Deeper understanding and experience using C for embedded development
Stretch Goal – embed code in device and detect real time

## Slide 4: Equipment
1) 1x STMicroelectronics SensorTile board.
2) 1x STMicroelectronics Nucleo Board.
3) 1x Personal Computer with two USB type-A inputs OR you must have a powered USB hub.
4) 1x USB 2.0 A-Male to Micro-B Cable (micro USB cable).
5) 1x USB 2.0 A-Male to Mini-B Cable (mini USB cable).
6) Network access to the Internet.
7) A Linux machine (Beaglebone, Intel Edison, Rpi, and etc)
8) 1x STMicroelectronics SensorTile Cradle+

## Slide 5: Proof Of Concept
There is no need for a POC, as there are several examples of freefall detectors like this full product (no longer for sale).

## Slide 6: Algorithm
When the normalized data changes from approximately 1g to 0g’s, a free fall is in progress
Normalization formula =

## Slide 7: Data Collection & Model
Capture data via the Bluetooth gatttool using a raspberry pi w
Convert raw hex data into decimal and save to file
Filter out unnecessary or bad data
Use support vector machine linear regression model using python scikit-learn

## Slide 8: Results, Conclusion, and Future work
100% of freefalls in test data were detected
Conclusion: Freefalls are easily detectable. When to act after a freefall starts is questionable. Just because a freefall condition is detected, doesn’t mean it’s an actionable fall (for example to deploy a safety device for a cell phone free fall)
Future work: Determine if there’s an algorithm to determine when a free fall is actionable. Confirm if additional acceleration data or gyroscope data can further delineate a free fall